## Slide 1: Hardware design basics
as viewed by a software person
(part 1)

## Slide 2: Motivation?
Knowing hardware FPGA design basics can help with better understanding limitations and capabilities of FPGA technology
From the software developer perspective, CPU is a black-box that is:
  Executing instructions
  Loading data from the memory
  Storing results back to memory
  Accessing IO devices
  Etc
  What’s happening inside a black-box is a MAGIC

## Slide 3: CPU hardware is a magic!
mov eax, ebx
add edx, ecx
lea edx, [edi+358h]
cmpxchg
xor eax, eax

## Slide 4: Digital circuits - basics
Works with two distinguishable signal levels: LOW and HIGH
LOW represents logical 0, HIGH represent logical 1
The whole circuit is a majestic play of zeroes and ones
TTL typical voltage levels:
  voltage between 0V and 1.5V represents LOW
  voltage between 3.5V and 5V represents HIGH
  Anything in between 1.5V and 3.5V is invalid (and can cause circuit damage)
CMOS typical voltage levels:
  voltage between 0V and 0.8V represents LOW
  voltage between 2V and 3.3V represents HIGH
  Anything in between 0.8V and 2V is invalid (and can cause circuit damage)

## Slide 5: Transistor – the basic element of the circuit
In a nutshell transistor is an electronically controlled “switch”
Multiple types of transistors do exist
MOSFET (metal oxide semiconductor field effect transistor) transistors are the most commonly used in a modern day electronics

## Slide 6
MOSFET transistor © Wikipedia

## Slide 7: MOSFET
There are two sub-types of MOSFETs:
pMOS
nMOS

## Slide 8: One level of abstraction up – logical gates
On a higher level, digital circuits are built of logical gates
Logical gates are built from transistors (and other elements in some cases)
Logical gates have one or more inputs
Let’s use letters A, B… (or a, b, …) to represent values of the inputs
Logical gates have just one output, let’s represent its value with ‘F’

## Slide 9: Logical gates
Gate: Function Symbol(s)
NOT F = not A
AND F = A and B and …
OR F = A or B or …
XOR F = A xor B xor …
NAND F = not (A and B and …)
NOR F = not (A or B or … )
XNOR F = not (A xor B xor …)
Image credits – Wikipedia

## Slide 10: How are gates implemented?

## Slide 11
Image credits – Wikipedia

## Slide 12: nMOS NOT gate – operation explained
Image credits – Wikipedia
0V
0V
0V
+3.3V
+3.3V
+3.3V
+3.3V
≈ 0V
Simulation: https://www.youtube.com/watch?v=U6QOOi0UGKE

## Slide 13
Image credits – Wikipedia

## Slide 14: nMOS NAND gate – operation explained
Image credits – Wikipedia
0V
0V
+3.3V
+3.3V
0V
0V
+3.3V
+3.3V
+3.3V
0V

## Slide 15: nMOS NAND gate – operation explained
Image credits – Wikipedia
0V
0V
+3.3V
+3.3V
+3.3V
0V
+3.3V
+3.3V
+3.3V
≈ 0V
Simulation:
https://www.youtube.com/watch?v=itNyruGdjzA

## Slide 16
Image credits – Wikipedia

## Slide 17: Problems with nMOS (and similar with pMOS)
Power consumption in idle
Resistors are too big for micro-chips
Complementary-MOS or CMOS to the rescue!

## Slide 18: CMOS NOT gate
Image credits – Wikipedia

## Slide 19: CMOS NOT gate – operation explained
Image credits – Wikipedia
+3.3V
0V
+3.3V
+3.3V
0V
0V
0V
+3.3V
Simulation video: https://www.youtube.com/watch?v=RJP3yPLblQ4

## Slide 20: CMOS NAND gate
Image credits – Wikipedia

## Slide 21: CMOS NAND gate – operation explained
Image credits – Wikipedia
0V
+3.3V
0V
0V
+3.3V
0V
+3.3V
0V
+3.3V
0V
+3.3V
+3.3V
+3.3V
0V
+3.3V

## Slide 22: CMOS NAND gate – operation explained
Image credits – Wikipedia
0V
+3.3V
+3.3V
+3.3V
+3.3V
Simulation video: https://www.youtube.com/watch?v=Yjwf5rUbDxs

## Slide 23: NAND/NOR logic
Any other gate type could be represented only with NAND gates only
Similar applies to NOR gates
NAND/NOR gates are easier to manufacture in hardware
Thus, it is often easier to build the whole chip with only NAND or with only NOR gates
Image credit: https://www.tutorialspoint.com/vlsi_design/vlsi_design_combinational_mos_logic_circuits.htm

## Slide 24
==AND
==OR
Image credits: Wikipedia: https://en.wikipedia.org/wiki/NAND_logic

## Slide 25
==NOR
==XOR
Image credits: Wikipedia: https://en.wikipedia.org/wiki/NAND_logic

## Slide 26: Combination circuits

## Slide 27: Combinational circuits
A “black box” implementing certain logical function
Output depends only on the current inputs (after the signal propagates through the gates)

## Slide 28: Combinational circuits
Combinational circuit can be fully defined in a table form
Let’s consider the following function defined by the table:
A | B | C | X | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
For every combination of input values (A, B, C), we explicitly define the output values X and Y.

## Slide 29
In a programming language word we would have defined this function as something like:
X = ((A==0 && B==0 && C == 1) ||
(A==0 && B==1 && C == 0) ||
(A==1 && B==0 && C == 0) ||
(A==1 && B==1 && C == 1)) ? 1 : 0;
Or treating A, B, C, X, Y as Booleans (and using math notation):
And similar way we can write Y:
A | B | C | X | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 30
We can already build the circuit based on equations above directly mapping and / or functions into gates
But these are sub-optimal and would result inefficient circuit
We must optimize the expressions first
Many ways do exist, not going to deep details, let’s just use the simple formula transformation for our simple case:

## Slide 32
We’ve just created a binary full adder circuit!
C_out,S = A + B + C_in
A | B | C_in | S | C_out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 33: Combining 1-bit adders and N-bit
It is slow
Image credits: https://en.wikipedia.org/wiki/Adder_(electronics)#Ripple-carry_adder

## Slide 34: Carry look ahead adder
Image credits: https://en.wikipedia.org/wiki/Carry-lookahead_adder
It is faster

## Slide 35: Another example:
Let’s define a combinatory circuit that would:
Has three inputs: signals A, B and S
Has one output Z, depending on S:
If S == 0, output equals A
If S == 1, output equals B
Such circuit has its own given name:
multiplexer or MUX
And it has its own symbol
multiplexer - MUX

## Slide 36: MUX
In table form we can define the MUX operation as follows:
Note that we only have 4 rows instead of expected 8, and there are also subtly coloured “-” cells,
Symbol “-” means “don’t care”, or “any value of signal would match this line”
A | B | S | Z
0 | - | 0 | 0
1 | - | 0 | 1
- | 0 | 1 | 0
- | 1 | 1 | 1

## Slide 37: MUX
A | B | S | Z
0 | - | 0 | 0
1 | - | 0 | 1
- | 0 | 1 | 0
- | 1 | 1 | 1
In a similar way to binary adder, we can derive the logical expression for the circuit output from the table:
Note that “-” values are ignored, this is an equivalent to writing the full equations as both pairs of “do not care” values were present and then simplifying the equation:

## Slide 38: MUX

## Slide 39: 4-1 MUX
Image credit: Wikipedia

## Slide 40: A bit of VHDL
(That’s why we are all here, right?)

## Slide 41: VHDL: brief intro
Let’s introduce VHDL by giving some example code and explaining what it does, but first…
The most important thing you need to know about VHDL:
VHDL abbreviation stands for:
  Very
  High
  Speed
  Integrated
  Circuit
  Hardware
  Definition
  Language
(there is nested abbreviation: VHDL == VHSIC HDL)

## Slide 42: VHDL: brief intro
Developed by U.S. Department of Defence with the initial purpose of documenting of circuit behaviour
Later adopter for other uses, e.g. synthesis of circuit from the definition
Syntax is based on ADA programming language (another beautiful child of DoD, no irony here)
Mandatory Hello World in ADA:
Both ADA and VHDL are super-strictly typed military grade languages
(start fearing now!)

## Slide 43: VHDL brief intro
Far not the only Hardware Definition Language in existence or use, other alternatives:
  Verilog
  SystemVerilog
  C-dialects (!)
  Others
Rumours are that VHDL is more popular amongst FPDA developers, Verilog is more popular in ASIC (Application Specific Integrated Circuit) world
VHDL Language itself is quite big and complex, but we don’t have to learn it all to understand the basics

## Slide 44: VHDL terminology by contrast with SW
Design – FPGA engineers convert caffeine into design
Synthesis – “compilation”, process of converting VHDL code into a netlist
Signal – “variable” (not quite exactly, but very-very roughly)
Variable – “variable”
Entity – “interface”
Architecture – “implementation of the interface”
Component == Entity + it’s architecture
Already feel confused?

## Slide 45: VHDL by example
Lets get back to our 1-bit adder
It is a classical example of “entity”
Entity has a “port” - number of input / output / bidirectional signals it uses to interface with the rest of the world
Those signals are the only way it interfaces with the outer world
In our adder example we have signals A, B, C_in, C_out and S

## Slide 46
VHDL - One bit adder – dataflow (or RTL) model implementation

## Slide 47
VHDL - One bit adder – structural model implementation

## Slide 48
VHDL – both adders together

## Slide 49
VHDL – both adders together - synthesis

## Slide 50
Side note: how you should actually do addition in VHDL

## Slide 51: VHDL – MUX2

## Slide 52: VHDL – MUX4

## Slide 53: Bistables
When the state is important..

## Slide 54: Bistables – Triggers and Flip-Flops
Consider the circuit:
What would be the values of signals A and B?
0
1

## Slide 55: Bistables – Triggers and Flip-Flops
Real world is not symmetrical, thus circuit would eventually resolve into one of the stable states:
These states are stable and self-supporting
0
1

## Slide 56: Bistables – Triggers and Flip-Flops
Let’s now add two switches connecting to zero signals A and B when pressed
This way we can now control the state by forcing one or another side into zero level
It is a bit brutal
It is how SRAM (static RAM) works
Simulation videos:
https://www.youtube.com/watch?v=ytM9lqsXwxk
https://www.youtube.com/watch?v=Si_8qexyEfU
(as an opposite to byte brutal)

## Slide 57: Latches
Image credits: https://en.wikibooks.org/wiki/Electronics/Flip_Flops

## Slide 58: SR latch
Image credits: https://en.wikibooks.org/wiki/Electronics/Flip_Flops

## Slide 59: SR latch - operation
Image credits: https://en.wikibooks.org/wiki/Electronics/Flip_Flops
Simulation video: https://www.youtube.com/watch?v=mKkE1hGsxHE
0
1
R = 1 changes nothing
Now R is back to 0, and S =1
Bottom gate out flips to zero
Zero propagates…
Upper gates flips to one
And it propagates too
Now if we remove S=1, circuit stays in it state
The circuit is now stable

## Slide 60: Gated SR latch
Image credits: https://en.wikibooks.org/wiki/Electronics/Flip_Flops

## Slide 61: D latch
Simulation video: https://www.youtube.com/watch?v=PnkENqnPqd8
Image credits: https://en.wikibooks.org/wiki/Electronics/Flip_Flops

## Slide 62: Flip-flops: D flip flop
Simulation video: https://www.youtube.com/watch?v=fain2HVHdp4

## Slide 63: D flip-flop: 1 bit register

## Slide 64: D flip flop in VHDL?

## Slide 65: D flip flop in VHDL?

## Slide 66: Other flip-flop types
JK flip-flop
Similar to SR, but inputs named J and K:
J=1, K=0 sets output to 0
J=0, K=1 sets output to 0
But J=1 and K=1 inverts current output on the next clock
T flip flop
One input – T
If T=0, nothing happens
If T=1, output is inverted on the next clock edge
Commonly implemented as JK flip flop with signals J and K connected to each other
Image source and further reading: https://www.electronics-tutorials.ws/sequential/seq_2.html
NOTE: Timing-sensitive design.
Clock pulse must be short, otherwise FF would trigger again for J=K=1

## Slide 67: The Master-Slave JK Flip Flop
Image source and further reading: https://www.electronics-tutorials.ws/sequential/seq_2.html

## Slide 68: Flip Flop Conversion
Example: T from D
Further reading: https://www.allaboutcircuits.com/technical-articles/conversion-of-flip-flops-part-iv-d-flip-flops/

## Slide 69: Flip flop usage examples: freq. division (by 2)
Source and further reading: https://www.electronics-tutorials.ws/counter/count_1.html

## Slide 70: VHDL implementation: freq. division (by 2)

## Slide 71: Flip flop usage examples: Async counter

## Slide 72: Flip flop usage examples: shift register
Source and further reading: https://www.electronics-tutorials.ws/sequential/seq_5.html

## Slide 73: Sequential circuits
(Finally some real stuff!)

## Slide 74: Sequential circuits
Consider our combinatory circuit black box

## Slide 75: Finite State machines: Moore

## Slide 76: Finite State machines: Moore
A finite set of states S
A start state S0
A finite set of inputs
A finite set of outpus
A transition function T
An output function G

## Slide 77: Finite State machines: Mealy
Very similar to Moore, but output is a function of both current state and current input
Less popular in FPGA design as it is harder to verify / validate

## Slide 78: Moore by example
Let’s design a state machine that would detect a sequential “111” bit pattern and start outputting ‘1’ after detecting such.
We would need four states:
  S0 – initial
  S1 – seen one ‘1’
  S2 – seen two ‘1’s
  S3 – seen three or more ‘1’s
Current State, S | Next state if I == 0 | Next state if I == 1 | Circuit output, O
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1

## Slide 79: Moore by example
We would need two bit’s to encode the state as we have four states, so now change states to values:
  S0 – 00
  S1 – 01
  S2 – 10
  S3 – 11
  This is pretty much a combinatory function definition table
S[1] | S[0] | I == 0, next val |  | I == 1, next val |  | O
 |  | Sn[1] | Sn[0] | Sn[1] | Sn[0] | 
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 1 | 1

## Slide 80: Moore by example
Sn[1] table:
S[1] | S[0] | I == 0, next val |  | I == 1, next val |  | O
 |  | Sn[1] | Sn [0] | Sn[1] | Sn[0] | 
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 1 | 1
S[1] | S[0] | I | Sn[1]
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
Sn[0] table:
S[1] | S[0] | I | Sn[0]
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
Output table
S[1] | S[0] | 0
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 81: Moore by example
Sn[1] table:
S[1] | S[0] | I | Sn[1]
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
Note: this can be done easier using Karnaugh map: https://en.wikipedia.org/wiki/Karnaugh_map

## Slide 82: Moore by example
Sn[0] table:
S[1] | S[0] | I | Sn[0]
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
Note: this can be done easier using Karnaugh map: https://en.wikipedia.org/wiki/Karnaugh_map

## Slide 83: Moore by example
Output table
S[1] | S[0] | 0
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Note: this can’t be done easier using Karnaugh map: https://en.wikipedia.org/wiki/Karnaugh_map

## Slide 84: Moore by example

## Slide 85: Alternative implementation with JK Flip Flop
Different types of flip flops can be more or less efficient for particular purpose
How is it done? Let’s see
NOTE: SKIP UNLESS EVERYONE IS EXCITED….

## Slide 86: Alternative implementation with JK Flip Flop
Further reading on FSM: ch.9 of “Introduction to Digital Systems: Modeling, Synthesis, and Simulation Using VHDL”
by Mohammed Ferdjallah, ISBN: 9780470900550, available in Safari Books
Same as before: do the state transition table, encode states as bits
After finding out how bits should change in each particular transition, we must calculate flip-flop inputs to toggle correct flip flop value toggle.
  E.g. gate network must produce correct values for J and K inputs, rather just ‘D’ inputs
The same can be done with T Flip Flops.

## Slide 87: Alternative implementation with JK Flip Flop
Further reading on FSM: ch.9 of “Introduction to Digital Systems: Modeling, Synthesis, and Simulation Using VHDL”
by Mohammed Ferdjallah, ISBN: 9780470900550, available in Safari Books
Let’s examine all the possible bit transitions and find out what J and K values has to be applied, again “-” means “do not care”:
From | To | J | K | Comment
0 | 0 | 0 | - | If K=0, FF state stays the same. If K=1, FF is again set to 0, which in fact is not changing its state
0 | 1 | 1 | - | If K=0, FF is set to ‘1’ by J=1, if K=1 FF is toggled by J=K=1, result is again 1
1 | 0 | - | 1 | If J=0, FF state is set to 0 by K=1, if J=1, FF state is toggled by J=K=1, result is 0
1 | 1 | - | 0 | If J=0, FF state didn’t change. If J=1, FF state is set to 1, that was already the value of the FF

## Slide 88: Alternative implementation with JK Flip Flop
Taking the bit transition / J/K values table, lets update our original state transition table with values for J and K:
From | To | J | K
0 | 0 | 0 | -
0 | 1 | 1 | -
1 | 0 | - | 1
1 | 1 | - | 0
S[1] | S[0] | I == 0, next val |  |  |  |  |  | I == 1, next val |  |  |  |  |  | O
 |  | Sn[1] | J[1] | K[1] | Sn[0] | J[0] | K[0] | Sn[1] | J[1] | K[1] | Sn[0] | J[0] | K[0] | 
0 | 0 | 0 | 0 | - | 0 | 0 | - | 0 | 0 | - | 1 | 1 | - | 0
0 | 1 | 0 | 0 | - | 0 | - | 1 | 1 | 1 | - | 0 | - | 1 | 0
1 | 0 | 0 | - | 1 | 0 | 0 | - | 1 | - | 0 | 1 | 1 | - | 0
1 | 1 | 0 | - | 1 | 0 | - | 1 | 1 | - | 0 | 1 | - | 0 | 1
The beauty of “-” aka “do not care” cells is that we can pick any value that simplifies our circuit / formula the best way.
This is best to be done using Karnaugh map: https://en.wikipedia.org/wiki/Karnaugh_map

## Slide 89: Alternative implementation with JK Flip Flop
Or let’s do it by hand as drawing Karnaugh map is harder than writing formulas in Microsoft Power Point
S[1] | S[0] | I == 0, next val |  |  |  |  |  | I == 1, next val |  |  |  |  |  | O
 |  | Sn[1] | J[1] | K[1] | Sn[0] | J[0] | K[0] | Sn[1] | J[1] | K[1] | Sn[0] | J[0] | K[0] | 
0 | 0 | 0 | 0 | - | 0 | 0 | - | 0 | 0 | - | 1 | 1 | - | 0
0 | 1 | 0 | 0 | - | 0 | - | 1 | 1 | 1 | - | 0 | - | 1 | 0
1 | 0 | 0 | - | 1 | 0 | 0 | - | 1 | - | 0 | 1 | 1 | - | 0
1 | 1 | 0 | - | 1 | 0 | - | 1 | 1 | - | 0 | 1 | - | 0 | 1

## Slide 90: FSM: state encoding matters
There are multiple ways our states S0…SN can be encoded in binary form, some produce more optimal gate networks
Some other types of flip flops can also produce more optimal gate networks
Different approaches can be used for state encoding, for example “one hot” where N states are encoded by N bits, where S0 represents 10000….0, S1 represents 01000….0, S2 – 00100….0 and so on, where SN is 0000..0001.
Latter can be produce more optimal results in some cases
Important: since we write VHDL and not designing circuits by hands, we don’t have to worry about the most efficient way of encoding, synthesis tool would optimise it for us.
Further reading: ch.9 of “Introduction to Digital Systems: Modeling, Synthesis, and Simulation Using VHDL”
by Mohammed Ferdjallah, ISBN: 9780470900550, available in Safari Books

## Slide 91: Moore by example – VHDL implementation

## Slide 92: Moore by example – VHDL implementation
, x)

## Slide 93: VHDL synthesis - Intel

## Slide 94: Synthesis –Technology Map – Intel

## Slide 95: Synthesis –Technology Map – Intel
Essential part of the circuit:

## Slide 96: Synthesis –Technology Map – Intel
Note: at any state, x=0 sets , and into 0, so let’s consider the state progression for a x=1 for a number of consecutives ticks:
Time | S0 | S1 | S3 | x | Sn0 | Sn1 | Sn3 | Out
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
2 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
3 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Key point: synthesis tool can heavily optimise the circuit out, but the resulting behaviour remains the same

## Slide 97: Another FSM example: 4-bit counter equivalent
Let’s now try building the state machine with 16 states S0…S15 and one input x
When x=0, machine state doesn’t change
When x=1, machine state moves to the next one: S0 to S1, .. S7 to S8, etc. If state was S15, machine goes back to S0 and process moves on
Output would be set equal to the current state encoded as binary
We would be using T Flip Flops – apparently this type of FSM can be very efficiently implemented using T FF.
Similar way to JK implementation, gate network must produce value for T flip flop input that would cause correct resulting state: T=1 if we need to toggle current value of a state bit, T=0 if we must keep it.
(not a flying spaghetti monster)

## Slide 98: FSM design example: 4-bit counter equivalent
S | Sn or x=0 | Sn for x=1
S0 | S0 | S1
S1 | S1 | S2
S2 | S2 | S3
S3 | S3 | S4
S4 | S4 | S5
S5 | S5 | S6
S6 | S6 | S7
S7 | S7 | S8
S8 | S8 | S9
S9 | S9 | S10
S10 | S10 | S11
S11 | S11 | S12
S12 | S12 | S13
S13 | S13 | S14
S14 | S14 | S15
S15 | S15 | S0
S | Sn or x=0 | T for x=0 | Sn for x=1 | T for x=1
0000 | 0000 | 0000 | 0001 | 0001
0001 | 0001 | 0000 | 0010 | 0011
0010 | 0010 | 0000 | 0011 | 0001
0011 | 0011 | 0000 | 0100 | 0111
0100 | 0100 | 0000 | 0101 | 0001
0101 | 0101 | 0000 | 0110 | 0011
0110 | 0110 | 0000 | 0111 | 0001
0111 | 0111 | 0000 | 1000 | 1111
1000 | 1000 | 0000 | 1001 | 0001
1001 | 1001 | 0000 | 1010 | 0011
1010 | 1010 | 0000 | 1011 | 0001
1011 | 1011 | 0000 | 1100 | 0111
1100 | 1100 | 0000 | 1101 | 0001
1101 | 1101 | 0000 | 1110 | 0011
1110 | 1110 | 0000 | 1111 | 0001
1111 | 1111 | 0000 | 0000 | 1111

## Slide 99: FSM design example: 4-bit counter equivalent: T0
S | T for x=1
0000 | 0001
0001 | 0011
0010 | 0001
0011 | 0111
0100 | 0001
0101 | 0011
0110 | 0001
0111 | 1111
1000 | 0001
1001 | 0011
1010 | 0001
1011 | 0111
1100 | 0001
1101 | 0011
1110 | 0001
1111 | 1111

## Slide 100: FSM design example: 4-bit counter equivalent: T1
S | T for x=1
0000 | 0001
0001 | 0011
0010 | 0001
0011 | 0111
0100 | 0001
0101 | 0011
0110 | 0001
0111 | 1111
1000 | 0001
1001 | 0011
1010 | 0001
1011 | 0111
1100 | 0001
1101 | 0011
1110 | 0001
1111 | 1111
0
1
1
0
0
1
1
0
1
0
1
0
0
1
1
0

## Slide 101: FSM design example: 4-bit counter equivalent: T2
S | T for x=1
0000 | 0001
0001 | 0011
0010 | 0001
0011 | 0111
0100 | 0001
0101 | 0011
0110 | 0001
0111 | 1111
1000 | 0001
1001 | 0011
1010 | 0001
1011 | 0111
1100 | 0001
1101 | 0011
1110 | 0001
1111 | 1111
0
0
1
0
0
0
1
0
0
0
1
0
0
1
0
0

## Slide 102: FSM design example: 4-bit counter equivalent: T3
S | T for x=1
0000 | 0001
0001 | 0011
0010 | 0001
0011 | 0111
0100 | 0001
0101 | 0011
0110 | 0001
0111 | 1111
1000 | 0001
1001 | 0011
1010 | 0001
1011 | 0111
1100 | 0001
1101 | 0011
1110 | 0001
1111 | 1111
0
0
0
0
0
0
1
0
0
0
1
0
0
0
0
0

## Slide 103: FSM design example: 4-bit counter equivalent: summary
This circuit is called “synchronous counter”

## Slide 104: Sync vs Async counters

## Slide 105: Time to get serious
Tired? Would certainly be soon!

## Slide 106: Ethernet Preamble
Now let’s try creating a design that would detect a pattern of 56 bits of alternating 1s and 0s
When such pattern is detected – output single ‘1’ and return into waiting state
If pattern is broken mid-pattern – for simplicity we return into wait / idle state
Creating 56-ish different states for this FSM would be impractical
Thus, we would need variables, or more precisely – counters, to minimise total number of states
Note: a sequence of 56 alternating 1s and 0s is a preamble of the ethernet frame

## Slide 107: Approximate software-ish implementation:
Proceed with implementing a Moore, treating the current counter value as sort of external input into the FSM
FSM must generate control bits to increment/clear counter value
If we use counter value and Moore’s state for producing output, it would be still in fact Moore FSM as counter is internal to the design

## Slide 108: FSM: eth preamble
Thus, state transition table would be as follows, let’s denote x for the value of the input bit and ‘cnt’ for the value of the counter:
For cnt we need 5-bit register, as its value is not exceeding 31.
We compare for == 28 (11100 in binary) by simply doing:
(where are individual bits of the counter, and is a “summary” signal)
State | Next State |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 | cnt /= 26 x=0 | cnt /= 26 x=1 | cnt = 26 x=0 | cnt = 26 x=1 |  |  | 
IDLE | IDLE | SEEN_1 | IDLE | IDLE | 0 | 0 | 1
SEEN_0 | IDLE | SEEN_1 | DET_PATTERN | DET_PATTERN | 0 | 0 | 0
SEEN_1 | SEEN_0 | IDLE | SEEN_0 | IDLE | 0 | 1 | 0
DET_PATTERN | IDLE | IDLE | IDLE | IDLE | 1 | 0 | 0
State | Next State |  |  |  |  |  | 
 | cnt /= 26 x=0 | cnt /= 26 x=1 | cnt = 26 x=0 | cnt = 26 x=1 |  |  | 
IDLE | IDLE | SEEN_1 | IDLE | IDLE | 0 | 0 | 1
SEEN_0 | IDLE | SEEN_1 | DET_PATTERN | DET_PATTERN | 0 | 0 | 0
SEEN_1 | SEEN_0 | IDLE | SEEN_0 | IDLE | 0 | 1 | 0
DET_PATTERN | IDLE | IDLE | IDLE | IDLE | 1 | 0 | 0

## Slide 109: FSM: eth preamble
Current State |  | Next State |  |  |  |  |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 |  | cnt /= 26 (=0) x=0 |  | cnt /= 26 (=0) x=1 |  | cnt = 26 (=1) x=0 |  | cnt = 26 (=1) x=1 |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Current State |  | Next State |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
:
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 110: FSM: eth preamble
Current State |  | Next State |  |  |  |  |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 |  | cnt /= 26 (=0) x=0 |  | cnt /= 26 (=0) x=1 |  | cnt = 26 (=1) x=0 |  | cnt = 26 (=1) x=1 |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Current State |  | Next State |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
:
0
0
1
1
0
0
0
0
0
0
0
0
1
0
0
1

## Slide 111: FSM: eth preamble
Current State |  | Next State |  |  |  |  |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 |  | cnt /= 26 (=0) x=0 |  | cnt /= 26 (=0) x=1 |  | cnt = 26 (=1) x=0 |  | cnt = 26 (=1) x=1 |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Current State |  | Next State |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 112: FSM: eth preamble
Current State |  | Next State |  |  |  |  |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 |  | cnt /= 26 (=0) x=0 |  | cnt /= 26 (=0) x=1 |  | cnt = 26 (=1) x=0 |  | cnt = 26 (=1) x=1 |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Current State |  | Next State |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 113: FSM: eth preamble
Current State |  | Next State |  |  |  |  |  |  |  | Main output, | Increment counter enable, | Reset counter enable,
 |  | cnt /= 26 (=0) x=0 |  | cnt /= 26 (=0) x=1 |  | cnt = 26 (=1) x=0 |  | cnt = 26 (=1) x=1 |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Current State |  | Next State |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 114: FSM: ethernet preamble

## Slide 115: FSM: eth preamble: final circuit
cnt
cnt==28

## Slide 116
And it works!
https://www.youtube.com/watch?v=7Z_RSm85cQk
Note: created with http://everycircuit.com/
Note: the circuit on the video has a few insignificant differences:
There is a small bug – it checks for ==23 instead of ==28 (my bad)
Condition for counter increment was initially set as , but it doesn’t work well with sync counter. This was later fixed to remove ‘X’ from the equation. Simulation tool only supports async ctrs with no clock – it works for that type of a counter

## Slide 117
Let’s now implement it in VHDL
We would implemented two separate versions
First version would be the exact replica of what our manual circuit does – very low structural level
Second version would be a more high level VHDL implementation
After that we would run both in parallel to compare outputs

## Slide 118: First version, counter module

## Slide 119: Ethernet preamble: first version, counter module

## Slide 120: Ethernet preamble: first version, “== 28” module

## Slide 121: Ethernet preamble: first version, main module

## Slide 122: Ethernet preamble: synthesis

## Slide 123: Ethernet preamble: second version, high level, declarations

## Slide 124: Ethernet preamble: second version, high level, process

## Slide 125: Ethernet preamble: second version, synthesis
Same logic, but different implementation

## Slide 126: Ethernet preamble: second version, state machine

## Slide 127: Ethernet preamble: second version, synthesis, Xilinx
Same logic, but different implementation

## Slide 128: LEVELUP!!
WE’VE UNLOCKED
VARIABLES

## Slide 129: Testbench: declarations

## Slide 130: Testbench: code

## Slide 131: Testbench: RUN