## Slide 1: Hardware design basics
as viewed by a software person
(part 2)
This presentation (along with the sample code) lives on github: https://github.com/quarck/vhdl_intro

## Slide 2: VHDL – a bit more formal introduction
Strictly typed language
Types of VHDL objects:
  constant
  variable
  signal
  file (we would ignore this one)
Object definition:
<Object type> <name> : <data type> [:= Initial value];

## Slide 3: VHDL: example object definitions
constant MATH_PI : real := 3.1415927;
variable ctr : integer :=0;
signal Q : bit := ‘0’;
Note: signal assignment is different between variables and signals (on purpose, we would cover it later):
Q <= not Q;
ctr := ctr + 1;

## Slide 4: VHDL – a bit more formal: basic types
type bit is (‘0’, ‘1’);
type boolean is (false, true);
type character is (NUL, SOH, … ‘ ’, ‘!’, … ‘A’, ‘B’, … ‘a’, ‘b’, …);
type integer is range -2.147.483.647 to 2.147.483.647; -- particular implementations may extend this range
type real is range -1.0e38 to 1.0e38; -- particular implementations may extend this range

## Slide 5: VHDL – a bit more formal: basic types
subtype natural is integer range 0 to integer'high;
subtype positive is integer range 1 to integer'high;
type string is array (positive range <>) of character;
type bit_vector is array (natural range <>) of bit;

## Slide 6: VHDL – a bit more formal: types
std_logic is a library defined type:
type std_logic is (
‘U’, -- Uninitialized
‘X’, -- Forcing unknown
‘0’, -- Forcing 0
‘1’, -- Forcing 1
‘Z’, -- High impedance
‘W’, -- Weak unknown
‘L’, -- Weak 0
‘H’, -- Weak 1
‘-’ -- Don’t care
};

## Slide 7: VHDL – a bit more formal: physical types
By example, system time type:
type time is range 0 to 1e20
units
fs;
ps = 1000 fs;
ns = 1000 ps;
us = 1000 ns;
ms = 1000 us;
sec = 1000 ms;
min = 60 sec;
hr = 60 min;
end units time;

## Slide 8: VHDL: arrays, example
type ram_t is array (0 to 255)
of std_logic_vector(7 downto 0);
signal ram : ram_t :=
(others => (others => '0’));
type bit_vector is array (natural range <>)
of bit;

## Slide 9: VHDL: arrays, example
type ram_t is array (0 to 255) of std_logic_vector(7 downto 0);
signal ram : ram_t := (others => (others => '0'));
-- Xilinx-specific: can be also peppered with:
attribute ram_style: string;
attribute ram_style of ram : signal is "distributed";
-- or
attribute ram_style of ram : signal is “block";
-- or
attribute ram_style of ram : signal is “auto";

## Slide 10: VHDL: records (structs), example
type t_TO_FIFO is record
wr_en : std_logic;
wr_data : std_logic_vector(7 downto 0);
rd_en : std_logic;
end record t_TO_FIFO;

## Slide 11: VHDL: operations: relational
Operation | Comment
= | 
/= | Not equal
< | 
<= | 
> | 
>= | 

## Slide 12: VHDL: operations: logic
Operation | Comment
and | 
or | 
nand | a nand b = not (a and b)
nor | a nor b = not (a or b)
xor | exclusive or
not | 

## Slide 13: VHDL: operations: Arithmetic
Operation | Comment
+ | 
- | 
* | 
/ | 
** | Power
mod | 
rem | 
abs | 

## Slide 14: VHDL: operations: Concatenation
Operation | Comment
& | 
signal a : std_logic_vector (7 downto 0) := “00000000”;
signal b : std_logic_vector (8 downto 0);
…
b <= ‘0’ & a; -- makes 8-bit signal into 9-bit

## Slide 15: VHDL: design units
Entity
Architecture
Package
Configuration (we would skip this one for now)

## Slide 16: VHDL: entity, formal syntax
entity <id> is
[<generic>];
[<ports>];
[<declarations>];
[begin <sentences>];
end [entity] [<id>];

## Slide 17: VHDL: entity - example
entity MUX21 is
port(
A : in bit;
B : in bit;
Ctrl : in bit;
Z : out bit;
end MUX21;

## Slide 18: VHDL: entity, example with generics
entity MUX21n is
generic( n : integer := 2);
port( A : in bit_vector(n-1 downto 0);
B : in bit_vector(n-1 downto 0);
Ctrl : in bit;
Z : out bit_vector(n-1 downto 0));
end MUX21;

## Slide 19: VHDL: architecture, formal syntax
architecture <id> of <id_entity> is
[<declarations>];
begin
<concurrent sentences>;
end [architecture] [<id>];

## Slide 20: VHDL: architecture, code example:
architecture Behaviour of MUX21n is
begin
process(A, B, Ctrl)
begin
if Ctrl = ‘0’ then
Z <= A;
else
Z <= B;
end if;
end process;
end Behaviour;

## Slide 21: VHDL: package
Declaration:
package <identifier>
[<declarations>];
end [package] [<identifier>]
Body:
package body <identifier>
[<Assignments and Detailed definitions>];
end [package body] [<identifier>]

## Slide 22: VHDL: package usage
Usage:
use <library>.<package name>.[<identifier> | all];
Example standard packages:
  std_logic_1164
  std_logic_arith
Used as follows:
  library ieee;
  use ieee.std_logic_1164.all;
  use ieee.std_logic_arith.all;

## Slide 23: VHDL: concurrent & sequential statements
Two types of code statemtns:
  Concurrent
  Sequential
All the VHDL code is concurrent by default
Unless it resides inside the “process” statement (also applies to “procedure” and “function” declarations)
Anything inside “process” statement is sequential

## Slide 24: VHDL: concurrent statements
All the lines of code are “executed” simultaneously
Example:
signal a : std_logic := ‘1’;
signal b : std_logic := ‘0’;
begin
-- code below swaps bit values between a and b
a <= b when rising_edge(clk);
b <= a when rising_edge(clk);
end …;

## Slide 25: VHDL: sequential statements
Code inside the “process” statement behaves as if it was just a regular software thread, “executing” line by line
Each “process” is executing in parallel with other processes
Synthesis tool would analyse the behaviour and produce the netlist that implements the required behaviour
A lot of sequential code statements cannot be synthesised, but can be used in testbenches, for example:
  wait for 20ns;

## Slide 26: VHDL: process (sequential statements):
Syntax:
[label:]
process [(<sensitivity list>)]
begin
<sequential sentences>
[<wait statements>;]
end process;
Either sensitivity list or at least one wait statement must be present.

## Slide 27: VHDL: process, sensitivity list:
Sequential statements inside “process” block are re-run each time any signal in the sensitivity list changes its value
(Process statement is executed once unconditionally at “start”)
Example:
process (clk, x)
begin
if rising_edge(clk) then
z <= x;
end if;
end process;

## Slide 28: VHDL: process, wait statement:
“Wait” statement suspends execution of the process until the wait condition is met
Can have simply a list of signals, in such case it is an equivalent to a sensitivity list Example:
process
begin
if rising_edge(clk) then
z <= x;
end if;
wait on clk, x;
end process;

## Slide 29: VHDL: process, wait statement:
Formal syntax:
[label:] wait [on <signal> {, ...}]
[until <boolean_expresion>]
[for <time_expresion>];
Examples:
wait on clk, x;
wait for 10 ns;
wait until clk = ‘1’;
wait; -- “terminates” the process

## Slide 30: VHDL: process, signals vs variables
Both “signals” and “variables” can be used inside the process statement
Variable assignment has an immediate effect
Signal assignment only “applies” when process is suspended

## Slide 31: VHDL: process, signals vs variables, example:
process
variable a : std_logic = ‘0’;
signal b : std_logic = ‘1’;
begin
if rising_edge(clk) then
a := y; -- value of ‘a’ is changed immediately
b <= y; -- value of ‘b’ is ‘cached’
if x = ‘1’ then
a := z; -- value of ‘a’ is changed again
b <= z; -- ‘b’ is still cached
end if;
end if;
wait on (clk, x, y, z); -- here ‘b’ is finally applied
end process;

## Slide 32: VHDL: process, signals vs variables
“signal” translates directly into a wire of flip-flop
“variable” gives some flexibility for the tool to analyse the behaviour and produce netlist that implements it, might as well get translated into the wire of flip-flop
“signal” can be viewed in the simulation waveform, while “variable” is usually not

## Slide 33: VHDL: Variable assignment (process only)
[label:] <variable name> := <expression>;

## Slide 34: VHDL: signal assignment
[label:] <signal_name> <= [delay_type] <expression> {after <delay>};
Can take quite complicated form, but these can be only used in testbenches:
A <= ‘0’, ‘1’ after 10 ns, ‘0’ after 15 ns, ‘1’ after 20 ns, ‘0’ after 30 ns, ‘1’ after 50 ns, ‘0’ after 70 ns;
B1 <= transport A after 10 ns;
B2 <= A after 10 ns;
B3 <= reject 5 ns A after 10 ns;
We would skip these ones

## Slide 35: VHDL: conditional signal assignment
[<label>:] <signal> <= [delay_type]
{<expression|waveform> when <boolean expression> else}
< expression|waveform> [when <boolean expression>];
Example:
z <= a when s = “00” else
b when s = “11” else
unnafected when others;

## Slide 36: VHDL: selective signal assignment
[<label>:]
with <expression> select
<signal> <= [delay_type]
{<expression|waveform> when <value>,}
<expression|waveform> when <value>;
Example:
with opcode select
res <= A + B when “00”,
A - B when “01”,
A and B when “10”,
A or B when “11”;
WOW! We’ve just implemented a very basic ALU (arithmetic logic unit) by accident!

## Slide 37: VHDL: sequential stm, if-statements, formal syntax
[label:] if <condicion> then
<sentencias secuenciales>
{elsif <condicion> then
<sentencias secuenciales}
[else
<sentencias secuenciales>]
end if [label];

## Slide 38: VHDL: sequential stm, case-statements, formal syntax
[label:] case <expresion> is
{when <value1> =>
<sequential sentences>;}
{when <value2> =>
<sequential sentences>;}
[when others =>
<sequential sentences>;]
end case [label];

## Slide 39: VHDL: sequential stm, while loops
[label:] while <boolean_condition>
loop
<sequential sentences>
end loop [label];

## Slide 40: VHDL: sequential stm, for loops
[label:] for <repetition_control>
loop
<sequential sentences>
end loop [label];
example:
for i in 1 to 10 loop
<statements>;
end loop example;
Loop variable should not be declared in advance, its lifetime is limited to the loop body
‘to’ can be changed to ‘downto’ for going down instead of going up.

## Slide 41: VHDL: generate statements, ‘if’
Conditionally generate or skip a piece of definition, syntax:
<label>: if <condition>
generate
{<concurrent sentences>}
end generate;

## Slide 42: VHDL: generate statements, ‘if’
Example:
if_32_bit: if n = 32
generate
a: ALU_32_bit port map (…);
end generate;
if_lt32_bit: if n < 32
generate
a: ALU_simple port map (…);
end generate;
-- to ensure we’ve covered all cases, let’s assert a bit:
assert n <= 32 report “Only 1-32 bits are supported”
severity failure;

## Slide 43: VHDL: generate statements, “for”
Generates repeating blocks. Syntax:
<label>: for <range specification>
generate
{<concurrent sentences>}
end generate;

## Slide 44: VHDL: generate statements, ‘for’
Example:
gen_adder: for i in 0 to 31
generate
adder: full_adder
port map(
a => a(i), b => b(i),
c_in => carry(i),
S => res(i),
c_out => carry(i + 1));
end generate;

## Slide 45: VHDL: function, just a syntax
Declaration:
function <name> [(<parameters list>)] return <data_type>;
Definition:
function <name> [(<parameters list>)] return <data_type> is
{<declarative part>}
begin
{<sequential sentences>}
end [function] [<name>];
One or more “return [expression];” in here

## Slide 46: VHDL: procedure, just a syntax
Declaration:
procedure <name> [(<parameters list>)];
Definition:
procedure <name> [(<parameters list>)] is
{<declarative part>}
begin
{<sequential sentences>}
end [procedure] [<name>];

## Slide 47: FPGAs
First, let’s recall our state machines that we did already in the part 1

## Slide 48: Sequence 111 detection FSM

## Slide 49: Sync counter FSM

## Slide 50: Ethernet preamble detection FSM

## Slide 51: FPGAs..
Notice a pattern in all our state machines:
In consists of flip-flops paired with some combinatory circuit that defines the next state of the flip flop
Inputs into the combinatory circuit could be either current circuit’s input or the current value of the circuit flipflop(s) or both.
If we denote our combinatory circuits as black boxes, we can draw these state machines as (next slides):

## Slide 52: Sequence 111 detection, generalized

## Slide 53: Sync counter:

## Slide 54: Ethernet preamble detection

## Slide 55: FPGA
The pair of configurable logical function coupled with the flip-flop is basically an elementary construction of any FPGA, called “System Logic Cell” or “Configurable Logic Block” – CLB for short.
Configurable logical function is called LUT, implemented as a simple lookup table, can have between 3 and 6 inputs and 1 or several bits of output.
FPGA cell can be configured to bypass either LUT or flip-flop, acting as just a LUT on its own or as a D flip-flop
CLB might contain additional logic to accelerate addition operation, etc.
These CLBs are arranged into a huge arrays with configurable interconnects
NOTE: FPGAs are not the only programmable logic devices that do exist, but the most capable ones

## Slide 56: FPGA, simplified configurable logic block

## Slide 57: LUT structure

## Slide 58: FPGA: CLBs in a real world, Spartan 6 example
Xilinx Spartan 6, each CLB contains two “slices”
Each slice is approximately identical and includes actual programmable logic
There are three slice types on Spartan 6: SLICEM, SLICEL, SLICEX
Each type of slice contains a set of 6-input LUTs and 8 Flip-Flops
SLICEL and SLICEM also contain carry logic and wide multiplexers
SLCIEM also has Distributed RAM and Shift Registers on board.
Image, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 59: FPGA: Xilinx Spartan 6, SLICEX:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 60: FPGA: Xilinx Spartan 6, SLICEL:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 61: FPGA: Xilinx Spartan 6, SLICEM:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 62: Spartan 6, ¼ of SLICEX, configuration variants
Two pre-programmable muxes (ignore the clock one), 6 combinations all together
Let’s review these combinations

## Slide 63: Spartan 6, ¼ of SLICEX config., variant 1
One isolated FF with CX as input and CQ as output
LUT output O5 paired with FF into CMUX output
LUT output O6 connected directly to the slice output C

## Slide 64: Spartan 6, ¼ of SLICEX config., variant 2
One isolated FF with CX as input and CQ as output
LUT output O6 connected directly to output C
LUT output O5 connected directly to output CMUX
Another FF is unused

## Slide 65: Spartan 6, ¼ of SLICEX config., variant 3
One isolated FF with CX as input and CQ as output
LUT output O6 connected directly to both output C and CMUX
LUT output O5 is not used (perhaps this config. can help with routing in some cases)
Another FF is unused

## Slide 66: Spartan 6, ¼ of SLICEX config., variant 4
Both LUT outputs are fed through FF I
LUT output O5 paired with FF into CMUX output
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C (may be unused)

## Slide 67: Spartan 6, ¼ of SLICEX config., variant 5
LUT output O5 is now goes directly into CMUX
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C (may be unused)
One FF is unused

## Slide 68: Spartan 6, ¼ of SLICEX config., variant 6
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C, and into CMUX
One FF is unused, as well as LUT O5
Not sure if this combination is used and if so - how

## Slide 69: FPGA interconnects
A very generic FPGA architecture:
An ocean (sea, lake, puddle) of configurable logic blocks (“fabric”)
Connected by programmable interconnects
Often has various “silicon” components as well –hardware modules designed for particular function (e.g.: memory controllers, multipliers, CPU cores, etc)

## Slide 70: FPGA interconnects In the real world
This
Is Spartan! (Spartan 6, XC6SLX9,
1430 slices, 5720 luts, 11440 FFs)
Displaying:
Long lines (magenta)
Pin lines (green)
Switch matrixes (‘big’ squares)
Slices (tiny dots)
Local slice-level lines are not displayed

## Slide 71: FPGA interconnects In the real world
This Is Spartan! (Spartan 6, XC6SLX9,
1430 slices, 5720 luts, 11440 FFs)
Displaying:
Long lines (magenta)
Pin lines (green)
Switch matrixes (‘big’ squares)
Slices (tiny dots)
Local slice-level lines (white mess)

## Slide 72: Spartan 6 XC6SLX9 structure, only slices
Only CLBS and the “eth preamble” bitstream routes are displayed
Key point: in the FPGA, most of the space is taken by the configurable routing / interconnects, and not by the logic cells

## Slide 73: Spartan 6 XC6SLX9, zoom in, local lines not displayed
Switch matrixes
Pin lines
Long lines
CLBs are too small to see here

## Slide 74: Spartan 6 XC6SLX9, further zoom in, no local lines
Switch matrixes
Slices (of CLB)

## Slide 75: Spartan 6 XC6SLX9, local lines displayed

## Slide 76: Spartan 6 XC6SLX9, further zoom in

## Slide 77: Spartan 6 XC6SLX9, further zoom in

## Slide 78: Spartan 6 XC6SLX9, at a max zoom
Switch matrixes
Two slices
Long Lines
Short Lines

## Slide 80: Time to reveal some magic?
“Final year project”

## Slide 81: Simple 8-bit CPU
Let’s now try to design a very simple 8-bit central processing unit
Once we understand the basics would carry on with more advanced designs
Design is based on “Ahmes” 8-bit CPU core (link in the appendix C), but the actual design went far from the original design.

## Slide 82: Our simple 8-bit CPU: architecture overview
von Neumann memory model – same memory for instructions and data (as opposite to Harvard commonly used in microcontrollers)
accumulator machine: single general purpose register called “accumulator”
  Any math/logical/etc instruction implicitly refers to the accumulator as the first argument
  Many “old days” computers were accumulator machines
    ENIAC (20 accumulators operating in parallel)
    PDP-8
    MOS 6502
    Intel 4004 and 8008 (modern day x86 has echoes of those days, for example “mul ecx” instruction would multiply registers “ecx” and “eax” and put result into pair of registers “eax” and “edx”)
    Intel 8051 microcontroller (this family is still in production and new derived chips are being produced these days)
  Thus, “accumulator machine” is not a sort of academic simplification of reality (aka “assume there no other bodies in the whole universe but two mass-points A and B”), but a production-used type of computers

## Slide 83: Our simple 8-bit CPU: architecture overview, cont.
8-bit address and data buses – can address only 256 bytes (hey, we are only playing here)
Simple 8-bit ALU with no multiply / divide operations
One register: 8-bit accumulator
Flags register: 4 flags
  n: negative – last ALU result was negative
  z: zero – last ALU result was zero
  c: carry – carry/borrow bit from the last ADD / SUB
  v: overflow – last ALU resulted in a signed overflow
~50 instructions all together (15 instructions in the “first cut”)
All instructions are encoded as 2-bytes for simplicity, first byte identifies operation, second byte – an argument

## Slide 84: Our simple 8-bit CPU: instruction set
Instruction | Action (C++-like syntax) | Comment
STA addr | mem[addr] = A | Store content of the accumulator into address ‘addr’
LDA addr | A = mem[addr] | Load accumulator with the content of memory address ‘addr’
LDC val | A = val | Load accumulator with direct value from the instruction

## Slide 85: Our simple 8-bit CPU: instruction set
Instruction | Action (C++-like syntax) | Comment
ADD addr | A += mem[addr] | 
ADDC addr | A += mem[addr] + carry | Add with the carry that was set by the previous operation
SUB addr | A -= mem[addr] | 
SUBC addr | A -= mem[addr] + carry | 
SUBR addr | A = mem[addr] - A | 
SUBRC addr | A = mem[addr] - A - carry | 
NEG | A = - A | Treats A as signed, inverts sign (Not a distinct instruction, just another name for “SUBR_V 0”)

## Slide 86: Our simple 8-bit CPU: instruction set
Instruction | Action (C++-like syntax) | Comment
ADD_V val | A += val | 
ADDC_V val | A += val + carry | Add with the carry that was set by the previous operation
SUB_V val | A -= val | 
SUBC_V val | A -= val + carry | 
SUBR_V val | A = val - A | 
SUBRC_V val | A = val - A - carry | 

## Slide 87: Our simple 8-bit CPU: instruction set, cont.
Instruction | Action (C++-like syntax) | Comment
OR addr | A ¦= mem[addr] | 
AND addr | A &= mem[addr] | 
XOR addr | A ^= mem[addr] | 
NOT | A = !A | (Not a distinct instruction, just another name for “XOR_V 255”)
SHR addr | A = ((unsigned)A) >> mem[addr] | 
SHL addr | A = A << mem[addr] | 
SHAR addr | A = ((signed)A) >> mem[addr] | 
ROL addr | TL;DR; | Rotate left by mem[addr]
ROR addr | TL;DR; | Rotate right mem[addr]
RCL addr | TL;DR; | Rotate through carry left mem[addr]
RCR addr | TL;DR; | Rotate through carry right mem[addr]

## Slide 88: Our simple 8-bit CPU: instruction set, cont.
Instruction | Action (C++-like syntax) | Comment
OR_V val | A ¦= val | 
AND_V val | A &= val | 
XOR_V val | A ^= val | 
SHR_V val | A = ((unsigned)A) >> val | 
SHL_V val | A = A << val | 
SHAR_V val | A = ((signed)A) >> val | 
ROL_V val | A = (A << val) ¦ (A >> (8-val)) | Rotate left by val
ROR_V val | A = (A >> val) ¦ (A << (8-val)) | Rotate right by val
RCL_V val | TL;DR; | Rotate through carry left by val
RCR_V val | TL;DR; | Rotate through carry right by val

## Slide 89: Our simple 8-bit CPU: instruction set
Instruction | Action (C++-like syntax) | Comment
JMP addr | pc = addr | Jump to address addr
JMP_A arg | pc = A + addr | Jump to address A + addr
JN addr | if (n==1) { pc = addr } | Jump to address if negative result (n=1)
JP addr | if (n==0) { pc = addr } | Jump to address if positive result (n=0)
JNZ addr | if (z == 0) { pc = addr } | Jump to address if non zero result (n=0)
JZ addr | if (z == 1) { pc = addr } | Jump to address if zero result (n=1)
JNC addr | if (c == 0) { pc = addr } | Jump to address if carry is not set (c=0)
JC addr | if (c == 1) { pc = addr } | Jump to address if carry is set (c=1)
JNV addr | if (v == 0) { pc = addr } | Jump to address if no overflow (v=0)
JV addr | if (v == 1) { pc = addr } | Jump to address if overflow (v=1)

## Slide 90: Our simple 8-bit CPU: instruction set
Instruction | Action (C++-like syntax) | Comment
IN port | A = io_port[port] | Read byte from I/O port
OUT port | io_port[port] = A | Write byte to I/O port
NOP | do {} while(false); | No operation, argument byte is unused
HLT | exit(0); | Full CPU stop until reset, argument byte is unused
SEVENSEGTRANSLATE |  | Performs table lookup to encode 4-bit number into 7-segment LCD display led configuration displaying given number

## Slide 91: Our simple 8-bit CPU: instruction set
On a first iteration, we would implement even simpler CPU that can handle only the following sub-set of instructions:
STA / LDA / LDC
ADD / ADDC / SUB / SUBC
OR / AND / NOT
JMP / JNZ / JZ
HLT / NOP
Such minimalistic CPU isn’t very practical, but works well for generating Fibonacci Sequence, thus let’s call it “Fibonacci Processing Unit”- FibPU
Our VHDL code would also include memory module, so in fact we are building a SoC – System on a Chip

## Slide 92: High-Level-Design

## Slide 93: Instruction execution cycle
FETCH
DECODE
EXECUTE
STORE

## Slide 94: types.vhd

## Slide 95: opcodes.vhd

## Slide 96: RAM – memory.vhd

## Slide 97: RAM – memory.vhd

## Slide 98: pio.vhd – does nothing in the first cut (just a stub)

## Slide 99: alu.vhd – getting closer…

## Slide 100: alu.vhd – architecture

## Slide 101: core.vhd – the control unit with registers

## Slide 102: core.vhd

## Slide 103: core.vhd

## Slide 104: core.vhd

## Slide 105: RAM access sequence
The moment “FETCH_0=>” block is result is applied:
Address bus set to ‘8’ (PC)
PC incremented by 1, now 9
The moment “FETCH_1 =>” block result is applied:
Address bus set to ‘9’
PC incremented by 1, now 9 (0xa)
Data requested at ‘FETCH_0’ (addr 8) arrives on the data bus (only usable on the next clk cycle)
The moment “DECODE =>” block result is applied:
Data requested at ‘FETCH_1’ (addr 9) arrives on the data bus (usable on the next clk cycle)

## Slide 106: core.vhd
NOTE:
This code would (probably?) generate Mealy FSM, since outputs - control selectors for various signals depend on both current state (DECODE) and current FSM input (data_in).
This should be OK though, as all inputs are internal for our circuit and data_in is synchronized to the same clock.

## Slide 107: core.vhd

## Slide 108: core.vhd

## Slide 109: core.vhd

## Slide 110: core.vhd
Back to ‘DECODE’:

## Slide 111: core.vhd

## Slide 112: core.vhd
Finally, the last bit

## Slide 113: TB_core.vhd – let’s test it
Nothing really there, we just create and link components, drive the clock signal and let the CPU run the code from the memory block

## Slide 114: RAM – memory.vhd – preloaded code

## Slide 115: TB_core.vhd – simulation run

## Slide 116: TB_core.vhd – simulation run – zoom in

## Slide 117: Can we do it without *HDL?
Se vi ege volas, vi povas. (Sed vi ne devus).

## Slide 118
State | Next State |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Outputs |  |  |  |  |  |  |  |  | 
 | OP: NOP | OP: STA | OP: LDA | OP: LDC | OP: ADD | OP: ADDC | OP: SUB | OP: SUBC | OP: OR | OP: AND | OP: NOT | OP: JMP | OP: JZ & Z=1 | OP: JZ & Z=0 | OP: JNZ & Z=1 | OP: JNZ & Z=0 | OP:HLT | ALU operation | Carry out | ALU left select | ALU right select | Addr select | Data out select | Mem write select | PC select | Accum select | Flags select
FETCH_0 | FETCH_1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FETCH_1 | DECODE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DECODE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_STA_1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_STA_2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_LDA_1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_LDA_2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_LDA_3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_LDC_1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_ALU_RM_1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_ALU_RM_2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_ALU_RM_3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E_JMP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
STORE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
STOP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GOOD LUCK! 

## Slide 119: Let’s look at the rest of the code

## Slide 120: types.vhd

## Slide 121: types.vhd

## Slide 122: opcodes.vhd

## Slide 123: opcodes.vhd

## Slide 124: opcodes.vhd

## Slide 125: opcodes.vhd

## Slide 126: core.vhd – remaining bits

## Slide 127: core.vhd – remaining bits

## Slide 128: core.vhd – remaining bits

## Slide 129: core.vhd – remaining bits

## Slide 130: core.vhd – remaining bits

## Slide 131: core.vhd – remaining bits

## Slide 132: alu.vhd – remaining bits

## Slide 133: alu.vhd – remaining bits

## Slide 134: memory.vhd – now with read_enable

## Slide 135: pio.vhd

## Slide 136: pio.vhd

## Slide 137: pio.vhd

## Slide 138: sevenseg.vhd

## Slide 139: sevenseg.vhd

## Slide 140: sevenseg.vhd

## Slide 141: sevenseg.vhd

## Slide 142: soc.vhd – simply linking everything together
It is boring…

## Slide 143: Program…

## Slide 145: Expected result?
002 003 005 008 00D 015 022 037 059 090 0E9 179 262 3DB 63D A18 055

## Slide 146: Finally…

## Slide 149: What I didn’t tell you?
Pure lack of time! No conspiracy here

## Slide 150: Items not covered
Timing
  Flip-Flop timings
  Whole design timing calculation / etc
Multiplier and Divider circuits
Clock domain crossing
Workflow of FPGA design (synthesis is only the first step)
IP components / libraries
User constraints
And a lot more… can’t fit everything into our format

## Slide 151: Appendix A. Xilinx Spartan 6 family summary
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 152: Appendix B. Xilinx Virtex Ultrascale family summary
© Xilinx, Source: https://www.xilinx.com/support/documentation/data_sheets/ds890-ultrascale-overview.pdf

## Slide 153: Appendix C. Further reading
http://www.simplecpudesign.com/simple_cpu_v1/index.html
https://blog.classycode.com/implementing-a-cpu-in-vhdl-part-1-6afd4c1ed491
http://embeddedsystems.io/ahmes-a-simple-8-bit-cpu-in-vhdl/