## Slide 1: Hardware design basics
as viewed by a software person
(part 2)
This presentation (along with the sample code) lives on github: https://github.com/quarck/vhdl_intro

## Slide 2: VHDL – a bit more formal introduction
Strictly typed language
Types of VHDL objects:
  constant
  variable
  signal
  file (we would ignore this one)
Object definition:
<Object type> <name> : <data type> [:= Initial value];

## Slide 3: VHDL: example object definitions
constant MATH_PI : real := 3.1415927;
variable ctr : integer :=0;
signal Q : bit := ‘0’;
Note: signal assignment is different between variables and signals (on purpose, we would cover it later):
Q <= not Q;
ctr := ctr + 1;

## Slide 4: VHDL – a bit more formal: basic types
type bit is (‘0’, ‘1’);
type boolean is (false, true);
type character is (NUL, SOH, … ‘ ’, ‘!’, … ‘A’, ‘B’, … ‘a’, ‘b’, …);
type integer is range -2.147.483.647 to 2.147.483.647; -- particular implementations may extend this range
type real is range -1.0e38 to 1.0e38; -- particular implementations may extend this range

## Slide 5: VHDL – a bit more formal: basic types
subtype natural is integer range 0 to integer'high;
subtype positive is integer range 1 to integer'high;
type string is array (positive range <>) of character;
type bit_vector is array (natural range <>) of bit;

## Slide 6: VHDL – a bit more formal: types
std_logic is a library defined type:
type std_logic is (
‘U’, -- Uninitialized
‘X’, -- Forcing unknown
‘0’, -- Forcing 0
‘1’, -- Forcing 1
‘Z’, -- High impedance
‘W’, -- Weak unknown
‘L’, -- Weak 0
‘H’, -- Weak 1
‘-’ -- Don’t care
};

## Slide 7: VHDL – a bit more formal: physical types
By example, system time type:
type time is range 0 to 1e20
units
fs;
ps = 1000 fs;
ns = 1000 ps;
us = 1000 ns;
ms = 1000 us;
sec = 1000 ms;
min = 60 sec;
hr = 60 min;
end units time;

## Slide 8: VHDL: operations: relational
Operation | Comment
= | 
/= | Not equal
< | 
<= | 
> | 
>= | 

## Slide 9: VHDL: operations: logic
Operation | Comment
and | 
or | 
nand | a nand b = not (a and b)
nor | a nor b = not (a or b)
xor | exclusive or
not | 

## Slide 10: VHDL: operations: Arithmetic
Operation | Comment
+ | 
- | 
* | 
/ | 
** | Power
mod | 
rem | 
abs | 

## Slide 11: VHDL: operations: Concatenation
Operation | Comment
& | 
signal a : std_logic_vector (7 downto 0) := “00000000”;
signal b : std_logic_vector (8 downto 0);
…
b <= ‘0’ & a; -- makes 8-bit signal into 9-bit

## Slide 12: VHDL: design units
Entity
Architecture
Package
Configuration (we would skip this one for now)

## Slide 13: VHDL: entity, formal syntax
entity <id> is
[<generic>];
[<ports>];
[<declarations>];
[begin <sentences>];
end [entity] [<id>];

## Slide 14: VHDL: entity - example
entity MUX21 is
port(
A : in bit;
B : in bit;
Ctrl : in bit;
Z : out bit;
end MUX21;

## Slide 15: VHDL: entity, example with generics
entity MUX21n is
generic( n : integer := 2);
port( A : in bit_vector(n-1 downto 0);
B : in bit_vector(n-1 downto 0);
Ctrl : in bit;
Z : out bit_vector(n-1 downto 0));
end MUX21;

## Slide 16: VHDL: architecture, formal syntax
architecture <id> of <id_entity> is
[<declarations>];
begin
<concurrent sentences>;
end [architecture] [<id>];

## Slide 17: VHDL: architecture, code example:
architecture Behaviour of MUX21n is
begin
process(A, B, Ctrl)
begin
if Ctrl = ‘0’ then
Z <= A;
else
Z <= B;
end if;
end process;
end Behaviour;

## Slide 18: VHDL: package
Declaration:
package <identifier>
[<declarations>];
end [package] [<identifier>]
Body:
package body <identifier>
[<Assignments and Detailed definitions>];
end [package body] [<identifier>]

## Slide 19: VHDL: package usage
Usage:
use <library>.<package name>.[<identifier> | all];
Example standard packages:
  std_logic_1164
  std_logic_arith
Used as follows:
  library ieee;
  use ieee.std_logic_1164.all;
  use ieee.std_logic_arith.all;

## Slide 20: VHDL: concurrent & sequential statements
Two types of code statemtns:
  Concurrent
  Sequential
All the VHDL code is concurrent by default
Unless it resides inside the “process” statement (also applies to “procedure” and “function” declarations)
Anything inside “process” statement is sequential

## Slide 21: VHDL: concurrent statements
All the lines of code are “executed” simultaneously
Example:
signal a : std_logic := ‘1’;
signal b : std_logic := ‘0’;
begin
-- code below swaps bit values between a and b
a <= b when rising_edge(clk);
b <= a when rising_edge(clk);
end …;

## Slide 22: VHDL: sequential statements
Code inside the “process” statement behaves as if it was just a regular software thread, “executing” line by line
Each “process” is executing in parallel with other processes
Synthesis tool would analyse the behaviour and produce the netlist that implements the required behaviour
A lot of sequential code statements cannot be synthesised, but can be used in testbenches, for example:
  wait for 20ns;

## Slide 23: VHDL: process (sequential statements):
Syntax:
[label:]
process [(<sensitivity list>)]
begin
<sequential sentences>
[<wait statements>;]
end process;
Either sensitivity list or at least one wait statement must be present.

## Slide 24: VHDL: process, sensitivity list:
Sequential statements inside “process” block are re-run each time any signal in the sensitivity list changes its value
(Process statement is executed once unconditionally at “start”)
Example:
process (clk, x)
begin
if rising_edge(clk) then
z <= x;
end if;
end process;

## Slide 25: VHDL: process, wait statement:
“Wait” statement suspends execution of the process until the wait condition is met
Can have simply a list of signals, in such case it is an equivalent to a sensitivity list Example:
process
begin
if rising_edge(clk) then
z <= x;
end if;
wait on clk, x;
end process;

## Slide 26: VHDL: process, wait statement:
Formal syntax:
[label:] wait [on <signal> {, ...}]
[until <boolean_expresion>]
[for <time_expresion>];
Examples:
wait on clk, x;
wait for 10 ns;
wait until clk = ‘1’;
wait; -- “terminates” the process

## Slide 27: VHDL: process, signals vs variables
Both “signals” and “variables” can be used inside the process statement
Variable assignment has an immediate effect
Signal assignment only “applies” when process is suspended

## Slide 28: VHDL: process, signals vs variables, example:
process (clk, x, y, z)
variable a : std_logic = ‘0’;
signal b : std_logic = ‘1’;
begin
if rising_edge(clk) then
a := y; -- value of ‘a’ is changed immediately
b <= y; -- value of ‘b’ is ‘cached’
if x = ‘1’ then
a := z; -- value of ‘a’ is changed again
b <= z; -- ‘b’ is still cached
end if;
end if;
wait on (clk, x, y, z); -- here ‘b’ is finally applied
end process;

## Slide 29: VHDL: process, signals vs variables
“signal” translates directly into a wire of flip-flop
“variable” gives some flexibility for the tool to analyse the behaviour and produce netlist that implements it, might as well get translated into the wire of flip-flo
“signal” can be viewed in the simulation waveform, while “variable” is usually not

## Slide 30: VHDL: Variable assignment (process only)
[label:] <variable name> := <expression>;

## Slide 31: VHDL: signal assignment
[label:] <signal_name> <= [delay_type] <expression> {after <delay>};
Can take quite complicated form, but these can be only used in testbenches:
A <= ‘0’, ‘1’ after 10 ns, ‘0’ after 15 ns, ‘1’ after 20 ns, ‘0’ after 30 ns, ‘1’ after 50 ns, ‘0’ after 70 ns;
B1 <= transport A after 10 ns;
B2 <= A after 10 ns;
B3 <= reject 5 ns A after 10 ns;
We would skip these ones

## Slide 32: VHDL: conditional signal assignment
[<label>:] <signal> <= [delay_type]
{<expression|waveform> when <boolean expression> else}
< expression|waveform> [when <boolean expression>];
Example:
z <= a when s = “00” else
b when s = “11” else
unnafected when others;

## Slide 33: VHDL: selective signal assignment
[<label>:]
with <expression> select
<signal> <= [delay_type]
{<expression|waveform> when <value>,}
<expression|waveform> when <value>;
Example:
with opcode select
res <= A + B when “00”,
A - B when “01”,
A and B when “10”,
A or B when “11”;
WOW! We’ve just implemented a very basic ALU (arithmetic logic unit) by accident!

## Slide 34: Side note: simple ALU, let’s see some code and netlists

## Slide 35: Side note: simple ALU, let’s see some code and netlists

## Slide 36: 32 bit? Behold!

## Slide 37: VHDL: sequential stm, if-statements, formal syntax
[label:] if <condicion> then
<sentencias secuenciales>
{elsif <condicion> then
<sentencias secuenciales}
[else
<sentencias secuenciales>]
end if [label];

## Slide 38: VHDL: sequential stm, case-statements, formal syntax
[label:] case <expresion> is
{when <value1> =>
<sequential sentences>;}
{when <value2> =>
<sequential sentences>;}
[when others =>
<sequential sentences>;]
end case [label];

## Slide 39: VHDL: sequential stm, while loops
[label:] while <boolean_condition>
loop
<sequential sentences>
end loop [label];

## Slide 40: VHDL: sequential stm, for loops
[label:] for <repetition_control>
loop
<sequential sentences>
end loop [label];
example:
for i in 1 to 10 loop
<statements>;
end loop example;
Loop variable should not be declared in advance, its lifetime is limited to the loop body
‘to’ can be changed to ‘downto’ for going down instead of going up.

## Slide 41: VHDL: generate statements, ‘if’
Conditionally generate or skip a piece of definition, syntax:
<label>: if <condition>
generate
{<concurrent sentences>}
end generate;

## Slide 42: VHDL: generate statements, ‘if’
Example:
if_32_bit: if n = 32
generate
a: ALU_32_bit port map (…);
end generate;
if_lt32_bit: if n < 32
generate
a: ALU_simple port map (…);
end generate;
-- to ensure we’ve covered all cases, let’s assert a bit:
assert n <= 32 report “Only 1-32 bits are supported”
severity failure;

## Slide 43: VHDL: generate statements, “for”
Generates repeating blocks. Syntax:
<label>: for <range specification>
generate
{<concurrent sentences>}
end generate;

## Slide 44: VHDL: generate statements, ‘for’
Example:
gen_adder: for i in 0 to 31
generate
adder: full_adder
port map(
a => a(i), b => b(i),
c_in => carry(i),
S => res(i),
c_out => carry(i + 1));
end generate;

## Slide 45: VHDL: function, just a syntax
Declaration:
function <name> [(<parameters list>)] return <data_type>;
Definition:
function <name> [(<parameters list>)] return <data_type> is
{<declarative part>}
begin
{<sequential sentences>}
end [function] [<name>];
One or more “return [expression];” in here

## Slide 46: VHDL: procedure, just a syntax
Declaration:
procedure <name> [(<parameters list>)];
Definition:
procedure <name> [(<parameters list>)] is
{<declarative part>}
begin
{<sequential sentences>}
end [procedure] [<name>];

## Slide 47: VHDL: arrays
TODO

## Slide 48: FPGAs
First, let’s recall our state machines that we did already in the part 1

## Slide 49: Sequence 111 detection FSM

## Slide 50: Sync counter FSM

## Slide 51: Ethernet preamble detection FSM

## Slide 52: FPGAs..
Notice a pattern in all our state machines:
In consists of flip-flops paired with some combinatory circuit that defines the next state of the flip flop
Inputs into the combinatory circuit could be either current circuit’s input or the current value of the circuit flipflop(s) or both.
If we denote our combinatory circuits as black boxes, we can draw these state machines as (next slides):

## Slide 53: Sequence 111 detection, generalized

## Slide 54: Sync counter:

## Slide 55: Ethernet preamble detection

## Slide 56: FPGA
The pair of configurable logical function coupled with the flip-flop is basically an elementary construction of any FPGA, called “System Logic Cell” or “Configurable Logic Block” – CLB for short.
Configurable logical function is called LUT, implemented as a simple lookup table, can have between 3 and 6 inputs and 1 or several bits of output.
FPGA cell can be configured to bypass either LUT or flip-flop, acting as just a LUT on its own or as a D flip-flop
CLB might contain additional logic to accelerate addition operation, etc.
These CLBs are arranged into a huge arrays with configurable interconnects
NOTE: FPGAs are not the only programmable logic devices that do exist, but the most capable ones

## Slide 57: FPGA, simplified configurable logic block

## Slide 58: LUT structure

## Slide 59: FPGA: CLBs in a real world, Spartan 6 example
Xilinx Spartan 6, each CLB contains two “slices”
Each slice is approximately identical and includes actual programmable logic
There are three slice types on Spartan 6: SLICEM, SLICEL, SLICEX
Each type of slice contains a set of 6-input LUTs and 8 Flip-Flops
SLICEL and SLICEM also contain carry logic and wide multiplexers
SLCIEM also has Distributed RAM and Shift Registers on board.
Image, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 60: FPGA: Xilinx Spartan 6, SLICEX:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 61: FPGA: Xilinx Spartan 6, SLICEL:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 62: FPGA: Xilinx Spartan 6, SLICEM:
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 63: Spartan 6, ¼ of SLICEX, configuration variants
Two pre-programmable muxes (ignore the clock one), 6 combinations all together
Let’s review these combinations

## Slide 64: Spartan 6, ¼ of SLICEX config., variant 1
One isolated FF with CX as input and CQ as output
LUT output O5 paired with FF into CMUX output
LUT output O6 connected directly to the slice output C

## Slide 65: Spartan 6, ¼ of SLICEX config., variant 2
One isolated FF with CX as input and CQ as output
LUT output O6 connected directly to output C
LUT output O5 connected directly to output CMUX
Another FF is unused

## Slide 66: Spartan 6, ¼ of SLICEX config., variant 3
One isolated FF with CX as input and CQ as output
LUT output O6 connected directly to both output C and CMUX
LUT output O5 is not used (perhaps this config. can help with routing in some cases)
Another FF is unused

## Slide 67: Spartan 6, ¼ of SLICEX config., variant 4
Both LUT outputs are fed through FF I
LUT output O5 paired with FF into CMUX output
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C (may be unused)

## Slide 68: Spartan 6, ¼ of SLICEX config., variant 5
LUT output O5 is now goes directly into CMUX
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C (may be unused)
One FF is unused

## Slide 69: Spartan 6, ¼ of SLICEX config., variant 6
LUT output O6 paired with FF into CQ output
LUT output O6 also connected directly into C, and into CMUX
One FF is unused, as well as LUT O5
Not sure if this combination is used and if so - how

## Slide 70: FPGA interconnects
A very generic FPGA architecture:
An ocean (sea, lake, puddle) of configurable logic blocks
Connected by programmable interconnects

## Slide 71: FPGA interconnects In the real world
This
Is Spartan! (Spartan 6, XC6SLX9,
1430 slices, 5720 luts, 11440 FFs)
Displaying:
Long lines (magenta)
Pin lines (green)
Switch matrixes (‘big’ squares)
Slices (tiny dots)
Local slice-level lines are not displayed

## Slide 72: FPGA interconnects In the real world
This Is Spartan! (Spartan 6, XC6SLX9,
1430 slices, 5720 luts, 11440 FFs)
Displaying:
Long lines (magenta)
Pin lines (green)
Switch matrixes (‘big’ squares)
Slices (tiny dots)
Local slice-level lines (white mess)

## Slide 73: Spartan 6 XC6SLX9 structure, only slices
Only CLBS and the “eth preamble” bitstream routes are displayed
Key point: in the FPGA, most of the space is taken by the configurable routing / interconnects, and not by the logic cells

## Slide 74: Spartan 6 XC6SLX9, zoom in, local lines not displayed
Switch matrixes
Pin lines
Long lines
CLBs are too small to see here

## Slide 75: Spartan 6 XC6SLX9, further zoom in, no local lines
Switch matrixes
Slices (of CLB)

## Slide 76: Spartan 6 XC6SLX9, local lines displayed

## Slide 77: Spartan 6 XC6SLX9, further zoom in

## Slide 78: Spartan 6 XC6SLX9, further zoom in

## Slide 79: Spartan 6 XC6SLX9, at a max zoom
Switch matrixes
Two slices
Long Lines
Short Lines

## Slide 83: Appendix A. Xilinx Spartan 6 family summary
© Xilinx, Source: https://www.xilinx.com/support/documentation/user_guides/ug384.pdf

## Slide 84: Appendix B. Xilinx Virtex Ultrascale family summary
© Xilinx, Source: https://www.xilinx.com/support/documentation/data_sheets/ds890-ultrascale-overview.pdf